## Slide 1
SCTE Virgin Media Taster Training Day
RMS RF Passive Electronic Components
Presented by: -
Christopher Bailey FSCTE
RMS Communications Europe Limited

## Slide 2
A Short History of RMS Communications Inc.
Business started in 1943
First Cable TV products introduced in the 1950’s
Head Office & Warehouse in Pineville NC USA
  RMS Branch Offices & Warehouses
Manufacturing Facilities
  Taiwan (Manufacturing Partners)
  China (Manufacturing Partners)
Distributors Worldwide
  Europe, South & Central America, Mexico, Asia & Middle East

## Slide 3
The Broadband Cable Communications Network

## Slide 4
Understanding the Fundamentals of Hybrid Fibre Coax (HFC) Network

## Slide 5
Typical Headend Racks
Typical CMTS
Head-end to Subscriber – Product Groups
Head-end
1GHz passive RF components may be used in the head-end

## Slide 6
Top Quality Passives for Headend Equipment
16 Way Splitter/Combiner

## Slide 7
The Coaxial Trunk & Feeder Distribution
RF Cable and RF Outdoor Line Passives
Economics and installed legacy coaxial cables require the use of these types of products
RF Line Passive
Front Cover
RF Line Passive
Internal Electronics

## Slide 8
8 Way, 1GHz Outdoor Tap
(Front View)
4 Way, 1GHz Outdoor Tap

## Slide 9
The Distribution Network & Hub – RF Outdoor Products
The hub is currently generally regarded as the demarcation point between optical fibre and coaxial cable. RF distribution is facilitated with a choice of distribution passive electronic components.
As with trunk distribution, outdoor line passives and taps (directional couplers) may be used where RF plant is not protected by cabinets or other forms of protective closure. Another reason to use outdoor passives to build this part of the network is where “power-passing” is required.
Most taps feature a “make-before-break” tap switch that ensures power and RF is never interrupted when the tap plate is removed.

## Slide 10
The Outdoor Tap Switch – How it Works....every time!
BYPASS SWITCH HELD FIRMLY IN PLACE WITH SCREWS ENSURE SMOOTH AND REPEATABLE OPERATION OF RELIIIABLE RF AND POWER SWITCH.
BERYLLIUM COPPER
“KS” CONNECTION
BLOCKS FOR CABLE
CENTRE CONDUCTOR
SIEZURE.
RMS TAP SWITCH IS CONNECTED TO THE BLOCKS, ENSURING CONTINUITY OF POWER AND RF THROUGH THE TAP IF TAP PLATE IS REMOVED.
A closed transition transfer switch is also called...
  ...a “make before break” switch.

## Slide 11
The Distribution Network – RMS Indoor/Outdoor Products
Where power passing is not a requirement, often the cost effective choice for RF distribution are indoor/outdoor RF passives.
Perhaps one of the most widely deployed RMS products of this type is the RMS 20V series.

## Slide 12
Cascading Indoor/Outdoor Taps...
With already several million homes passed with RMS tap panels, a truly cost effective design solution has been proven beyond any doubt!
Either 4 or 8 way taps cascaded with patent digital “U”-links.

## Slide 13
The Drop Network – Indoor RF Passive Products
Different operators refer to the drop network by various names including the “last mile” and the “subscriber drop”.
RF passive electronic components enable RF distribution from the hub or curb to the subscribers’ set-top boxes and cable modems.
Splitters – All configurations and types
Directional Couplers – All configurations and types
Galvanic Isolators
  Through (barrel & block), 2 and 3 way also with custom filter types

## Slide 15
Features & Benefits Required in DC’s & Splitters
Passband 5MHz – 1010MHz
Excellent low inter-modulation spec >-110dBc
SCTE/ANSI compliant
Micro-strip designed for consistency of specifications
Precision machined F ports
Excellent insertion & return loss
Excellent port to port isolation
Concave solder back design
FR4-G10 glass printed circuit board
Laminated ID label UV protected
RFI Shielding –120dB
Zinc housing that is triple plated

## Slide 16
Low Inter-modulation Tester

## Slide 17
The Drop Network
Here we focus on Galvanic Isolators: -
Surge protected to 5,000VDC, the galvanic isolator breaks electrical continuity (conduction) of both the inner and outer conductors of the coaxial cable, whilst maintaining an uninterrupted signal path and signal integrity
Galvanic isolators ensure electrical safety for both the network technician and subscriber.
Excellent RF isolation (RFI) is provided when using RF galvanic isolators, whether the simple barrel isolator or more complicated low-profile “block” type of isolator.

## Slide 18
RF Galvanic Isolators
It is often difficult to obtain good grounding in the street cabinet or outside plant. It is also highly unlikely that the subscriber’s utility ground (earth point) will be at the same earth potential as that of the network ground outside the subscriber’s home.
Connecting with the drop coaxial cable, two earths of differing potential results in “sheath currents”, that can be several hundred volts and harmful to both subscribers and network technicians.
The galvanic isolator also eliminates the possibility of accidentally (in the event of a fault), passing the subscriber’s utility supply power to the outside plant via the drop coaxial cable.

## Slide 19
Sheath Currents...What do you mean?
A sheath current is a form of electromagnetic wave in wires.
For example, they can run along the outer sheath of a coaxial cable. The return conductor is the outer conductor of the cable. This can be, for example, from a geographically proximate or remote ground potential.
Sheath currents may lower the efficiency of transmission and can interfere with nearby electronic devices. In addition, sheath currents caused by differences in ground potential at the ends of a coaxial cable to common mode signals that are superimposed on the useful signal as a noise voltage. Sheath currents can also be caused by ground loops.

## Slide 20
Barrel Isolator
Low Profile Isolator

## Slide 21
Subscriber Outlet Boxes – Example Box
Assembled Outlet Box

## Slide 22
SCTE Virgin Media Taster Training Day
THANK YOU!
RMS RF Passive Electronic Components