## Slide 1: HEVC & UHDTV New compression technologies
Oct 2014
Pre-Sales Engineer EMEA
i.stankovic@ateme.com
Igor Stankovic
Regional Sales Director
a.itzhaki@ateme.com
Adi Itzhaki

## Slide 2
HEVC and UHD definition & technologies
Market adoption, experiments & perspectives

## Slide 3
HEVC: 50% of bandwidth savings

## Slide 4
HEVC & UHDTV standards
HEVC: High Efficiency Video Coding
  Joint standard ITU-T Rec H.265 and ISO/IEC 23008-2 MPEG H Part 2
  Revisions and additions to come (Contribution, 3D, Scalability, Screen encoding...) will not affect broadcast applications.
UHDTV1: Aligned on HDMI 2.0 capabilities
  Up to 60 fps, up to 10-bit.
  5.1 audio, possibly AC4, no standard for object based audio
  HD color space = BT709, BT2020 is not mandatory, no HDR, no HFR
  Scalable to higher frame rates (Phase 2)
  No standard to carry uncompressed 4K (4 X 3G-SDI by default)
DVB is adding UHD and HEVC to its core specifications
  Final stages of editing for DVB-S, DVB-T and DVB-C
  It will be: TS 101 154 v1.12.1
  it will probably be replicated by SCTE, ATSC, etc...

## Slide 5
What are bringing the guidelines?
Ease interoperability:
  Only constant framerate
  Only 16:9 aspect-ratio
  Mandatory signaling to help decoders
Ensure compatibility with other standards
  MPEG Transport Stream
  SCTE for splicing capabilities (not finalized yet)
  SMPTE on UHD format and metadata
  Liaisons with ATSC and to ensure compatible guidelines
No major change in the broadcast chain
  Multiplexer, re-multiplexers, ad-inserters, splicers etc. are expected to be easily made compatible

## Slide 6
ATEME’s role in HEVC Standardization
ATEME is an active contributor to the HEVC standardization process
  Own contributions
  Joint contributions with various companies (e.g. Fujitsu, Sony, Orange, Harmonic, Technicolor, Toshiba,…)
ATEME is one of 5 active contributors to the DVB usage standard
Several technical contributions
  Parallelization tools: Wavefront and Tiles
  Intra coding tools
  High level syntax
  Professional considerations
  (10/12 bits, 4:2:2, 4:4:4)
  Profile considerations
  Interlaced support and coding tools
  White paper "HEVC & Broadcast Content" =>
ATEME has filed 4 patents on HEVC

## Slide 7
Defining 4kTV for our research purpose
We define 4kTV as 3840 x 2160 progressive (16/9)
  Also known as Quad Full HD
We assume a frame rate of 50 or 59.94 Hz
  A lower frame rate would not make sense
  It means overall 8 times more pixels per second than in 1080i HDTV
Pixel format: 4:2:2 10-bit ideally
  4:2:2 ease support of legacy content and improves text and CGI
  The benefit of 4:4:4 and 12-bit+ is modest for broadcast applications
We target up to 7.1 Audio
  It is already standardized by Digital Cinema
  It is the best audio rendering system that we can expect to be available and practical to install in the home in the next 2 years

## Slide 8
Hollywood studios (Fox, Warner etc.) are very much focused on 10-bit encoding (Main-10 profile). Why is it like that?
  10-bit compression provides a moderate compression efficiency gain (5%), very similar in HEVC and H.264.
  The human eye is very sensitive to certain colors, for instance dark blue. Consequently, compression artifacts in these color ranges are very visible and could be very annoying (banding artifacts). Using extra precision reduces these defects.
  Those extreme colors are not present using the standard HDTV color space (BT709), therefore banding artifact is very uncommon, even in 8-bit.
  But studios want to use an extended color space (BT2020) where those colors might be present therefore we need to avoid banding artifact => 10-bit is needed.
Why 10-bit is important in UHDTV?

## Slide 9
HEVC / 4EVER project
An ATEME initiative : We brought the consortium members together
4EVER – for Enhanced Video ExpeRience
French research consortium
3 year collaborative project
Multi-million € plan
Objectives:
  Research, develop and promote an Enhanced quality Television Experience.
  Premium content delivery for everyone
  Entire production and delivery chain to Home, Mobile and Cinema
  Thanks to:
    HEVC technology development and codec prototyping
    Ultra High Definition - 4KTV, format definition and qualification.

## Slide 10
HEVC / 4EVER project
Consortium partners : cover the entire production and delivery chain
Cooperation requests keep coming in to leverage the work of the consortium: TV Set manufacturers, Semiconductor providers, Telecom operators.

## Slide 11
HEVC decoding:
  HW UHDTVp60 chips are in preparation, 8 and 10-bit.
  Broadcom
  STMicroelectronics
  Mstar
  ViXS
  Qualcomm (p30)
  Hybrid & SW decoders in a variety of devices:
  LG, Samsung, Sony TVs
  Visualon on tablets
  OpenHEVC (open-source) integrated in VLC, GPAC, ATEME Player etc. on PC
  Rovi, Fraunhofer HHI decoders on PC
HEVC Decoders: status
Most of the decoding solutions are currently prototypes:
  ATEME works with all those vendors to ensure interoperability
  TVs and OpenHEVC aim at 10-bit, making them the most advanced decoder today

## Slide 12
Encoding technologies alternatives
3 technologies currently available:
CPU including SIMD instruction sets
Massive parallel processor array(Nvidia GPU, Intel Larrabee and successors, Kalray MPPA etc.)
Hardware encoding core embedded in processors (Intel Sandy Bride/Ivy bridge/Haswell)
Why is a software solution fit for HEVC?
Faster time-to-market
Fit with Industry expectations for flexibility and scalability
Future-proof solution with increasing performances
Notes: 12
12

## Slide 13
Example of HEVC new encoding tools
More complex - and more efficient coding tree structure:
PU
TU
64x64
8x8
CU

## Slide 14
Measured HEVC bitrate gains
Gains are highly dependent on the video sequence and its size, but are always impressive
  Using PSNR, in 720p, the average bitrate gain is 35%. Up to 50%.
  Gains are 15% more important in 4k than in VGA
These gains are based on TITAN (commercially available)
Chart: Soccer 720p50 ATEME EAVC4 H.264 vs H.265
| 2 | 4 | 8 | 16
H.264 | 33.291 | 34.5803 | 35.5427 | 36.6057
H.265 | 34.0898 | 35.5329 | 36.6159 | 37.7898
43% gain

## Slide 15
HEVC vs H.264 1080p@25fps encoded at 2.7 Mb/s
H.264
HEVC

## Slide 16
HEVC and UHD definition
Market adoption, experiments & perspectives

## Slide 17
HEVC market drivers
Existing applications and usage scenarios
  Telcos: Bring HD everywhere
    Increase HD IPTV eligibility for DSL clients (20%-80% ->80%-20%)
    More customers on the same infrastructure + Mobile viewers (4G)
  OTT and multi-screen services: Reduce CDN costs
    Reduced bandwidth & caching
    Preserved picture quality
  Cable/satellite/DTT: attract more customers, reduce churn
    More channels on same infrastructure
    Increase resolutions and frame rates
Future services
  1080p60/50 premium services with bitrates comparable to 1080i
  For OTT, 720P50/60 at the bitrate of current 720P25/30 streams
  Immersive viewing experience: UHDTV
  HD Everywhere…

## Slide 18
Market trends: screens are booming
Big Screen TV
Audience and revenue Mainstream
2nd Screens
Technology innovation
for leadership
SoLoMo
(Social Local Monetization)
For customer retention

## Slide 19
Apple embraces HEVC

## Slide 20
Impact on market adoption
EVENTS & FIELD
CONTRIBUTION
CONTENT
OWNERS &
BRODCASTERS
CABLE / TELCO / SATELLITE
TV / VOD / WEB / MOBILE
DISTRIBUTION
RE-DISTRIBUTION
MULTISCREEN
C/D UHD in MPEG-4
Open solution for event and regular production
Broadcast  UHD in HEVC
Bandwidth efficient solutions for customer reach

## Slide 21
3 WC matches were produced in 4K
HBS has communicated instructions to FIFA right holders regarding the 4K matches
This document was broadly communicated and names ATEME Kyrion DR5000 as one of two solutions that can be used to receive those feeds
HBS has selected the EBU for the international distribution of all 64 games of the FIFA WC, as well as the 4K production (3 matches)
As a result, Broadcasters around the world have received streams encoded by ATEME, and in many cases DR5000 receivers loaned or sold by EBU

## Slide 22
4K contribution in H.264 solution
CM5000 -2 HD-10
CM5000 -2 HD-10
MC3100 Multiplexer
DR5000 1080p50/60
MPTS
IP 80 Mbps
4K Live Uncompressed
4x 20Mbps services
4K Decoded
UHD-Lock® Synchronization
4 x 3G SDI (1080p50/60) Source - Synchronized
4 x 3G SDI (1080p50/60)

## Slide 23
French Open ’14 experiments – 1/2
France Televisions organized a large-scale HEVC UHDTV broadcast experiment during the French Open ’14
  Two weeks broadcast
  Two days dedicated to a mix of HD and UHD production (2 HD & 4 UHD cameras)
  Using available or “soon-to-be-available” products including cameras, production facilities, encoders, STB, transmission links and TVs
HEVC streams were made available on satellite, DTT and IP

## Slide 24
French Open ’14 experiments – 2/2
4 x 1080p50
3G-SDI inputs
UHDp50
@28Mbps
Transport Stream
DVB-S2
Eutelsat 5WA
UHDp50
@28Mbps
Eutelsat Teleport
Fiber (IP)
RG Lab
Eiffel Tower
Champ-de-Mars
Europe
UHD TVs
UHD TVs

## Slide 25
HEVC in Korean UHDTV Channel
Umax, a demonstration cable channel has been launched, April 10, 2014 by Homechoice, a leading content aggregator in South -Korea
  4Kp60 HEVC Main profile, TS @ 32 Mbps, 30.5 Mbps video
  Dolby stereo audio
  Running from 6 AM to 2 AM,
  with 40 original programs at launch, in loop,
  planning to ramp up to 100 programs in 2014
  Mix of films, documentaries, and sports (some up-converted from 30 to 60 fps);
  Funded & distributed free of charge by all South-Korean MSOs (CJ Hellovision, C&M, T-Broad, HCN)
3 free to air experimental licenses have just been granted to KBS, MBC and SBS
  Licenses from May to Dec 2014, coverage on metro Seoul (>25% of the population of South-Korea)
  Planning to experiment live 4KP60 broadcasting using DVB-T2, looking at 25 to 27 Mbps for video
  South-Korea hosted Asian games in Sept.2014 was a major highlight for KBS and MBC
  Fifa WC for SBS
In both cases, viewing is primarily on Samsung and LG HEVC capable UHDTVs

## Slide 26
UHDTV/HEVC perspectives
Good news:
  With HEVC, broadcast UHDTV quality at bitrates down to 11Mbps or 18Mbps upon the content complexity
  Interoperability seems to be much easier to achieve than with H.264/AVC
  Broadcast delivery needs little/no modification
  UHDp50/60 user experience is very promising!
Challenges:
  Gain 10% efficiency over the next couple of years - HEVC is in its infancy, H.264 is mature
  Interoperability based only on a “common understanding” between vendors
  4K availability led by content availability

## Slide 27
ATEME Overview
Leader in MPEG-2 MPEG-4 & HEVC video encoding and transcoding solutions for service providers, broadcasters, and content owners
Fastest growing company in the broadcast encoder market with revenues of
$28,5M in 2013
Up 50% Year-on-year since 2009
130 employees, from which 53 are in R&D.
Headquartered
near Paris with
offices worldwide

## Slide 28
Solution overview
SPORTS & NEWS
Software Transcoding
solutions for live & file
delivery workflows
CONTRIBUTION
BROADCASTER
Hardware {FPGA based} encoders and decoders
CABLE / TELCO / SATELLITE
TV / VOD / WEB / MOBILE
DISTRIBUTION
RE-DISTRIBUTION
MULTISCREEN
Broadcast Video Head-End
turnkey system provider

## Slide 29
Company History
Throughout ATEME’s history the company has been focused on video compression
Design house
& Codec Licensing
Encoders
launched at NAB
Designing video & signal processing systems Avionics
Providing Codec technology to ISVs and OEMS
First Kyrion
deployments in
IPTV over ADSL and
terrestrial broadcasting
First TITAN
deployments for premium Video
On Demand services; Live transcoding added in 2011.
TITAN ads support of resolutions up to 4K UHDTV and the new HEVC/H.265 compression standard
.
1991-2001
2007
2010
2013
2014
TITAN Live is the world’s first carrier-grade software multi-screen solution mixing IP and SDI on the same platform with HEVC and 4K.
DR5000 Integrated
Receiver Decoder launched at NAB
TITAN Live
Any-to-Any
Beginning of our partnership on the South African WC

## Slide 30
Thanks / Xвала / Hvala
Questions? / Питањa? / Pitanja?
End

## Slide 31
Backup slides

## Slide 32
H.264 vs HEVC: Seeing is believing

## Slide 33
No common definition of 4K TV
  4K TV should not only be a resolution, but also:
  Frame-rate
  Pixel coding (aspect ratio, gamut, color sampling and pixel bit-depth)
  Audio
  No common definition or international audio-video standard targeting Broadcast television beyond HD
  4k2k, Quad Full HD, 4K, Super HD, 4KTV, 4K cinema
  At least 3 definitions exist today:
  4K DCI (Digital Cinema Initiative): 4096x2160 pixels at 24 Hz (+up to 7.1 multi-channel)
  NHK Super Hi-Vision: Ultimate 2D A/V format: 7680x4320 pixels at 120 Hz (+ audio 22.2)
  UHDTV1 & UHDTV2 (ITU-R Draft): 3840x2160 and 7680 x4320, audio is out of scope

## Slide 34
UHDTV standardization
UHDTV Phase 1 is aligned on HDMI 2.0 capabilities
  Up to 60 fps, up to 10-bit
  5.1 audio, possibly AC4, no standard for object based audio
  BT709 = HD color space, BT2020 is not mandatory (means will not happen), no HDR, no HFR
  Scalable to higher frame rates (will be a constraint for UHDTV Phase 2 systems, no immediate consequence)
  For deployment from 2015
  At this time, still no standard to carry uncompressed 4K (using 4 X 3G-SDI by default)
UHDTV Phase 2 raises a lot of questions
  Currently foreseen for deployments from 2017
  Requires alignment with NHK's 8K ambitions
  Requires new standards for uncompressed audio and video

## Slide 35
Expected benefits from 4kTV
In our labs, our engineers needed to stand within 1.5 m of a 55” 4KTV set to tell the difference between 2K & 4K
Initial studies found that using a viewing distance of 2.7m (European average), it takes a 76 Inch screen to see the difference with HDTV
But NHK studies claim the gain can be perceived on much smaller screen sizes

## Slide 36
HEVC toolset versus H.264 and MPEG-2
 | MPEG-2 | H.264/AVC | HEVC
Partition size | Macroblock 16x16 | Macroblock 16x16 | Coding Unit 8x8 to 64x64
Partitioning | Inter 16x8, Intra 8x8 | Sub-block down to 4x4 | Prediction Unit Quadtree down to 4x4 Square, symmetric and asymmetric (only square for intra)
Transform | Floating DCT | Integer DCT 8x8, 4x4 | Transform Unit square IDCT from 32x32 to 4x4 + DST Luma Intra 4x4
Intra prediction | DC predictor | Up to 9 predictors | 35 predictors
Motion prediction | Vector from one Neighbor | Spatial Median (3 blocks) | Advanced Motion Vector Prediction AMVP (spatial + temporal)
« Motion-copy » mode | / | Direct mode | Merge mode
Motion precision | ½ Pixel bilinear | ½ Pixel 6-tap, ¼ Pixel bi-linear | ¼ Pixel 7or 8-tap, 1/8 Pixel 4-tap chroma
Entropy coding | VLC | CABAC, CAVLC | CABAC
Filters | / | Deblocking Filter | Deblocking Filter Sample Adaptive Offset
HEVC toolset versus H.264 and MPEG-2

## Slide 37
H.264 vs HEVC
Already demonstrated results (*):
  HEVC Main profile would enable the broadcast quality of UHDTV at video bitrates below 13Mbps
Results are confirmed with Main and Main 10:
  With HEVC, broadcast UHDTV quality at bitrates between 11Mbps and 18Mbps
  Same gain than between MPEG-2 and H.264/AVC
  (*) J. Viéron and M. Parmentier, "4K TV capture, an early experience sharing,” Proc SMPTE Conf, 2012.

## Slide 38
A lot of statements have been made over the past months on HEVC gain vs H.264. What our eyes are telling us right now :
  The bitrate gain in file, compared to our best H.264 is seen between 30% and 40%. The gain is higher in UHD than with smaller resolutions like 720p.
  The bitrate gain in live, compared to our best H.264 is seen between 20% and 30%. The gain is similar across the available resolutions.
It is not quite 50% yet - we still need to gain 10% efficiency over the next couple of years - HEVC is in its infancy, H.264 is mature
    We have worked continuously on H.264 since 2005
    Several tools in our HEVC can still be improved
    Public comparisons were made on reference models - not industrial solutions
    Reference models do not produce the best possible VQ
    Our EAVC4 MPEG-4 AVC is better than the equivalent reference model (JM) by about 5%. Our HEVC encoder is behind the equivalent model (HM) by about 5%
About HEVC relative performance

## Slide 39
Why is a software solution fit for HEVC?
=> Our H.264 experience makes us confident that we can get price & density of SW based HEVC in line with market expectations
Chart: 
| Q2 2011 | Q3 2011 SW release | Q4 2011 Westmere | Q1 2012 SW release | Q2 2012 SB | Q4 2012 EAVC4 | Q4 2013 MS by Design
# Live H.264 SD / blade | 4 | 6 | 9 | 10 | 15 | 20 | 30

## Slide 40
HEVC Encoding: ATEME's experience
CPU (Intel/AMD) vs GPU (NVIDIA/AMD) vs HW (Embedded HW encoders Intel)
Coding Efficiency (VQ)
Speed
Power Efficiency
Flexibility (speed / VQ tradeoffs)
Upgradability (ability to develop new algorithms)
Development affordability (low development cost)
Compatibility (among evolving hardware)
CPU
CPU
GPU
HW
CPU
GPU
HW
CPU
GPU
HW
CPU
GPU
HW
CPU
GPU
HW
GPU
HW
GPU
HW
CPU
Notes: 40
40

## Slide 41
4K Content studied to date
(a) Roland Garros (Red Epic) (b) Champs Elysées (Red Epic) (c) Le chien couché à ses pieds (Red Epic)
(d) Brest (Sony F65) (e) Paris (Sony F65) (f) Nantes (JVC GY-HMQ10)
(g) Crowdrun (Scanned film) (h) Ducks (Scanned Film) (i) Brest_cam (JVC GY-HMQ10)

## Slide 42
4K availability led by content availability
4K content availability roadmap (Future Source consulting, Jan 2014)

## Slide 43
Video figures explode from all perspectives
4K resolution is 4 times bigger than Full HD
4K need 50 or 60 frame per second for enhanced visual quality
Monthly IP traffic per application
Source CISCO VNI Feb 2014 –
Consumer
video
Consumer
File sharing
Business
Web & other data
Consumer
Web & Other data
Business
Video
Business
File sharing
Video traffic =
74% of IP traffic in 2017
Video figures explode

## Slide 44
Bandwidth challenges remain present
Estimated cost
for sending satellite
= $290M
Extract from State of the Internet report –
Q3 2013 - Akamai
Bandwidth availability is not progressing
as fast as customer demand for bigger resolution

## Slide 45
Redistribution scenario in HEVC
4 x HD-SDI 1080p60
inputs
4Kp60
@25Mbps
(mini.)
MPEG-2 TS
Built-in HEVC decoder
in TV sets
Real-time HEVC encoding
& Built-in Supervision
Terrestrial network
Satellite
network
Demodulation
Modulation
TITAN Live "Any-to-Any" supports the acquisition and encoding of an uncompressed UHD signal in HEVC Main Profile, up to 60 Frames per second
TITAN File can be used to perform offline encoding of the same, up to Main-10 profile

## Slide 46
ATEME successes in UHD and HEVC
FOOTBALL STADIUMS
Software Transcoding
solutions for live & file
delivery workflows
CONTRIBUTION
FIFA RIGHT HOLDERS
Hardware {FPGA based} encoders and decoders
CABLE / TELCO / SATELLITE
TV / VOD / WEB / MOBILE
DISTRIBUTION
RE-DISTRIBUTION
MULTISCREEN

## Slide 47
BBC Research : 4K lab experiment
BBC Research posted this on their blog
http://www.bbc.co.uk/rd/blog/2014/07/how-to-get-uhd-back-from-brazil
The FIFA 4K Games were used for lab experiments, but also for a VIP event at the top of the BT TOWER in London on the evening of the final match
The BBC already had equipment from Ericsson and NTT in their labs that could have been used
They preferred to secure the system with ATEME and purchased 2 DR5000 (and we loaned them 2 more)

## Slide 48
SBS Korea : DVB-T2 broadcasting
UHDp60
ASI out
Samsung, LG UHDTV
DVB-T2 demodulator integrated
@30Mbps
IP out
3840 x 2160
4 x 1080p60
inputs
Enensys
Modulator
IP to ASI gateway
SBS is using TITAN as primary encoder for terrestrial broadcasting (Envivio as 1st back-up, Rohde & Schwarz as second back-up)
SBS has also purchased a TITAN KFE license to prepare UHD content for playout (including rebroadcast of FIFA WC 4K games)

## Slide 49
NMS
PLAYOUT SERVER
An UHD Broadcast solution by ATEME
ANEVIA VIAMOTION
TITAN LIVE HEVC
8-Bit
(10-Bit roadmap)
UHD SDI CAPTURE
UHD ENCODED
CONTENT
REPOSITORY
TITAN FILE 10-Bit
UHD LIVE SOURCES
UHD FILE SOURCES
RAW FILE
HEVC FILE
HEVC 8-Bit
HEVC 8/10-Bit
TO INVESTIGATE

## Slide 50
HEVC dominant in 4K VOD
UHD Pack initiative by Samsung, in partnership with Hollywood majors
  A mix of 8 movies and documentaries initially, supplied on a 1TB USB device, that may then be renewed over IP from a choice of 50
  Video encoding is 4KP24 HEVC Main 10 profile, TS or MP4 @ 40 Mbps average (VBR), 60 Mbps peaks, considering DTS 5.1 for audio
  Clearly targets the same 'ultra high end' quality as the 4K/UHD
  Blu-ray disc specification for which work is ongoing
Streaming VOD services under preparation
  Netflix, Amazon Instant, M-GO expected this quarter
  Targeting 4KP24 at around 15 Mbps (CBR)
  Plans announced typically ramp up to 100 titles by end 2014
  Netflix would roll out HEVC for HD and SD as well at some point
The only 4K VOD services that would not use HEVC would
be Sony Video Unlimited 4K (MPEG-4) & Youtube (VP9)
Netflix 4K Demo at CES14, credit: Stuff